## Slide 3: CSA Tech Talk
Presented by:
Todd Kruse, Team 3840
Chris Roadfeldt, Team 4607

## Slide 4: Questions Answered
Who Are We?
What is CSA?
When should you contact a CSA?
How can you contact a CSA?
Firmware?
  How to check versions
  Loading firmware
How setup the RobotRIO
  Imaging for LabView, Java, C++

## Slide 5: Questions Answered
2017 Radio Setup
  Configuration Utility
Driver Station Overview
  Controls and debug help
Radio Configuration
Tips and Good Practices
  Troubleshooting, things to be aware

## Slide 6: Who we are?
Todd
  2018 is 5th season with FIRST
  Lead Electrical/Software Mentor for Team 3840
  Robot Inspector
  Lead C.S.A
Chris
  4th Season with FIRST
  Former Lead Controls Mentor, now Support Mentor for 4607
  Robot Inspector
  Lead C.S.A

## Slide 7: What is a CSA?
The FIRST Control System Advisor is a volunteer who assists teams with Robot Control System-related issues. Works in collaboration with the FIRST Technical Advisor and/or Robot Inspectors, who may direct teams experiencing issues on the field or in the pits to the CSA for assistance.

## Slide 8: What is a CSA?
Classic: Assist teams in correcting Robot Control System Issues such as those related to the roboRIO, support boards such as the Pneumatics Control Module, wiring, programming, sensors, driver station, and laptop-roboRIO interface
MN CSA: Assist teams on and off season with all aspects of robot controls. Eg; code language determination, training, 2nd opinions, etc…
Folks in the Orange Caps.

## Slide 9: When should you contact a CSA?
Classic: At events for support of control issues.
MN CSA: Whenever you have controls related question. Can also assist with some drivetrain related questions. On or Off season.
Wear Orange Caps.

## Slide 10: How can you contact a CSA?
Classic: Find the Orange Hats
MN CSA:
  Email: firstmn.csa@gmail.com - also opens a trello ticket.
  Slack: firstmncsa.slack.com – please request invite.
  Twitter: @firstmncsa
Additional Resources:
  First MN Website: http://mnfirst.org/first-community-resources/local-assistance/
  First MN CSA Github: https://github.com/firstmncsa
  First MN Google Drive: http://goo.gl/STtiAg

## Slide 11: Updating your roboRIO firmware
Enter the address 172.22.11.2 in your browser's address bar and press enter.
roboRIO-####-FRC.local, where #### is your team number)
The embedded web server on the roboRIO requires using a browser which supports Silverlight
Note that Google Chrome has removed Silverlight support, using Internet Explorer is recommended.
Note that Google Chrome has removed Silverlight support, using Internet Explorer is
recommended.
Getting Started with the 2016 Control System
Getting
Notes: Connect a USB cable from the roboRIO USB Device port to the PC. This requires a USB Type A male
(standard PC end) to Type B male cable (square with 2 cut corners), most commonly found as a
printer USB cable.

## Slide 12: Hero LifeBoat Imager by CTRE

## Slide 13: Updating your roboRIO firmware
Enter the address 172.22.11.2 in your browser's address bar and press enter.
2. Click Login. Enter
"admin" in the Username
field and leave the
Password field blank.
3. Click Update Firmware
Notes: Connect a USB cable from the roboRIO USB Device port to the PC. This requires a USB Type A male
(standard PC end) to Type B male cable (square with 2 cut corners), most commonly found as a
printer USB cable. The driver is for windows is installed during install of latest suite for current year.

## Slide 14: Locate Firmware
Browse to Program Files\National Instruments\Shared\Firmware\cRIO\76F2\ Program Files(x86) on 64 bit and select the latest firmware, then click Open (this image shows version 2.0.0f1).
Notes: Take a look at where the file is located at…Ensure latest suite is installed first.

## Slide 15: Updating Firmware On Other Devices
Notes: Ensure to load firmware for PDB, PCM Modules as well.

## Slide 16: Updating Firmware On Talon SRX’s
A Talon SRX can have a device ID from 0 to 62. 63 is reserved for broadcast. If you select an invalid ID you will get an immediate prompt.
Notes: Ensure to load firmware for PDB, PCM Modules as well.

## Slide 17: Updating Firmware On Talon SRX’s
Select the firmware file (*.crf) to flash.
Notes: Search windows for *.crf

## Slide 18: Updating Firmware On Talon SRX’s
Finished Successfully.
Notes: Search windows for *.crf

## Slide 19: Updating Firmware – PCM / PDP
Must update firmware on these devices
Notes: Demonstrate on electrical board.

## Slide 20: Imaging your roboRIO
Before imaging your roboRIO, you must have completed installation of the the development environment and language updates for the appropriate programming language (C++\Java, LabVIEW) and the FRC Update Suite. You also must have the roboRIO power properly wired to the Power Distribution Panel.

## Slide 21: Imaging your roboRIO
Note: The roboRIO should only be imaged via the USB connection. It is not recommended to attempt imaging using the Ethernet connection.

## Slide 22: roboRIO Imaging Tool
A desktop shortcut to the roboRIO Imaging Tool has been added, so it's much easier to find and use.

## Slide 23: roboRIO Imaging Tool
After launching, the roboRIO Imaging Tool will scan for available roboRIOs and indicate any found in the top left box. The bottom left box will show the available image versions that may be loaded onto the roboRIO. The right hand column contains information and settings for the roboRIO selected in the top left pane.

## Slide 24: Imaging the roboRIO
Make sure the roboRIO is selected in the top left pane
Enter your team number in the box in the top right
Make sure the Disable RT Startup App box is unchecked in the bottom right
Check the box to Format Target and select the latest image version in the box.
Click Reformat to begin the imaging process.

## Slide 25: Imaging Complete
When the imaging completes you should see the dialog above. Click Ok, then click the Close button at the bottom right to close the imaging tool. Reboot the roboRIO using the Reset button to have the new team number take effect.
Notes: Then download JRE or C++ Tool Change or LabView Plug-In’s

## Slide 26: Radio Configuration
If no ethernet interfaces are listed, click "Refresh" to re-scan for available interfaces
Select the interface you want to use from the drop-down list
3. Click "OK"

## Slide 27: Radio Configuration
1. Select which radio you are configuring using the drop-down list.
2. Select which operating mode you want to configure. For most cases,
the default selection of 2.4GHz Access Point will be sufficient. Note
that the 2.4GHz + 5GHz simultaneous AP mode is not supported by
the D-Link radios.
3. If located outside the USA, select the Country as well to program the
proper country specific restrictions

## Slide 28: Radio Configuration
Follow the on-screen instructions for preparing your wireless bridge, entering the settings the bridge will be configured with, and starting the configuration process. These on-screen instructions update to match the bridge model and operating mode chosen.

## Slide 29: Radio Configuration

## Slide 30: Driver Station
Follow the on-screen instructions for preparing your wireless bridge, entering the settings the bridge will be configured with, and starting the configuration process. These on-screen instructions update to match the bridge model and operating mode chosen.

## Slide 31: Driver Station
Notes: The FRC LabVIEW Dashboard is the default dashboard program installed with, and automatically launched by, the FRC Driver Station. The purpose of the Dashboard is to provide feedback about the operation of the robot. The FRC Default Dashboard serves as a an example of the types of feedback
teams may want from their robot.

## Slide 32: Message Console & Log Files

## Slide 33: Driver Station – SmartDashboard
Notes: The SmartDashboard is an alternate dashboard application written in Java. The SmartDashboard
automatically creates a widget for each variable sent from the Robot sent using the SmartDashboard
class or VIs. These widgets can be configured to a number of preset display types, or users can create
custom extensions in Java.

## Slide 34: Smart Dashboard – Live View

## Slide 35: Driver Station – Shuffleboard
Notes: The SmartDashboard is an alternate dashboard application written in Java. The SmartDashboard
automatically creates a widget for each variable sent from the Robot sent using the SmartDashboard
class or VIs. These widgets can be configured to a number of preset display types, or users can create
custom extensions in Java.

## Slide 36: Driver Station – Shuffleboard
Notes: The SmartDashboard is an alternate dashboard application written in Java. The SmartDashboard
automatically creates a widget for each variable sent from the Robot sent using the SmartDashboard
class or VIs. These widgets can be configured to a number of preset display types, or users can create
custom extensions in Java.

## Slide 37: Trouble Shooting
Power
• Green - Power is good
• Amber - Brownout protection
tripped, outputs disabled
• Red - Power fault, check user rails
for short circuit

## Slide 38: Trouble Shooting
Status
• On while the controller is booting, then
should turn off
• 2 blinks - Software error, reimage
roboRIO
• 3 blinks - Safe Mode, restart roboRIO,
reimage if not resolved
• 4 blinks - Software crashed twice without
rebooting, reboot roboRIO, reimage if
not resolved
• Constant flash or stays solid on –
Unrecoverable error

## Slide 39: Trouble Shooting
Comm
• Off - No Communication
• Red Solid - Communication with DS, but
no user code
• Red Blinking - E-stop
• Green Solid - Good communication with DS

## Slide 40: Trouble Shooting
Mode
• Off - Outputs disabled (robot in Disabled,
brown-out, etc.)
• Amber/Orange - Autonomous Enabled
• Green - Teleop Enabled
• Red - Test Enabled

## Slide 41: Trouble Shooting - PDP

## Slide 42: Trouble Shooting - VRM
The status LEDs on the VRM indicate the state of the two power supplies. If the supply is functioning properly the LED should be lit bright green. If the LED is not lit or is dim, the output may be shorted or drawing too much current.

## Slide 43: Trouble Shooting - PCM
Notes: Solenoid Channel LEDs - These LEDs are lit red if the Solenoid channel is enabled and not lit if it is disabled.
Comp - This is the Compressor LED. This LED is green when the compressor output is active
(compressor is currently on) and off when the compressor output is not active.
Status - The status LED indicates device status as indicated by the two tables above. For more
information on resolving PCM faults see the PCM User Manual. Note that the No CAN Comm fault will not occur only if the device cannot see communicate with any other device, if the PCM and PDP can
communicate with each other, but not the roboRIO you will NOT see a No Can Comm fault.

## Slide 44: Axis Camera Tool
The Setup Axis Camera utility is a LabVIEW program used to configure an Axis 206, M1011 or M1013 camera for use on the robot.

## Slide 45: Using the camera server on the roboRIO
The following program gets a CameraServer instance and starts automatic capture of a USB camera like the Microsoft LifeCam that is connected to the roboRIO.

## Slide 46: Tips and Good Practices: Reliability!
Most important consideration, bar none.
  Three most important parts of a robot are, famously, “controls, controls and controls.”
Good practices:
  Continuous to read weekly updates from FIRST
  Document IP Address and configuration settings
  Backup and store offline of main computer

## Slide 47: Resources
Getting Started with the 2017 Control System
  https://wpilib.screenstepslive.com/s/4485/m/13503
Configuring an Axis Camera
  https://wpilib.screenstepslive.com/s/4485/m/24194/l/144985-configuring-an-axis-camera?id=144985-configuring-an-axis-camera
FRC Driver Station Powered by NI LabVIEW
  http://wpilib.screenstepslive.com/s/4485/m/24192/l/144976?data-resolve-url=true&data-manual-id=24192